## Slide 1: PARC HB OPAMPS SIMPLIFIED (with LTSpice)
Dave VE3OOI
Feb 2021

## Slide 2: FOLLOW AND LEARN
This is not a “traditional” tutorial
Its “Hands-On”, experimental approach.
Build experience using LTSpice
Present a “Principal” then clarify with experiment with LTSpice

## Slide 3: FUNDEMANTALS
Based on a bunch of transistors
Have 2 inputs + (non-inverting) and – (inverting)
Have Positive Supply (+V) and a Negative Supply (-V). Lets call this positive or negative voltage “rails”
Output is based on difference.
  Output is 0 if difference between inputs is 0
  Generally, output a voltage between voltage rails based on difference of inputs

## Slide 4: Principal 1: Input Offset Voltage
If voltage at + input is greater than – input, output is set to Positive Rail
If voltage at - input is greater than + input, output is set to Negative Rail
Real opamp has input offset due to mismatched parts and tolerances.
  0 voltage difference applied to both terminal does NOT produce 0 volts output
  Typical offset between inputs to trigger output to hit Positive or Negative Rail
LT1013 is replacement of LM358

## Slide 5: Experiment 1: Input Offset Voltage
1.2mV at output. What input offset is needed?
  For Gain = 100, input = 1.201542/100 mV = 12 uV
An input offset of 12uV is needed to make output zero.
This is a simulation. Data sheet says typically 40 – 150 uV and due to MANUFACTURING.
Offset set to -12.0156µV

## Slide 6: Experiment 2: Input “Offset” Voltage
+ & - are equal so output = 0
Whatttt? Gain of 14V/40uV=350K or 615 dB
Huh?
HOMEWORK:
Vary the input. Is it linear between 0-40uV?
What happens if you ground the negative supply?
+ & - difference is input “offset” voltage
so output “should be” = Positive Rail

## Slide 7: Experiment 3: Alternate View of “Offset”
75uV
Opamp DOES NOT set output to positive or negative rail with a small offset. Huh?

## Slide 8: LTSPICE MINUTE: PULSE SOURCE

## Slide 9: Rail to Rail
Many opamps don’t swing to the voltage rails. This reduces the useful limit of an opamp. BEWARE!!
Opamps that swing to both rails are called “rail-to-rail” opamps
FINDING 1:
Opamps have a HUGE gain!
Small input voltage can create output close to or equal to rail voltage

## Slide 10: Experiment 4: Comparator
Can be used to identify when a voltage is below, at or above a reference voltage

## Slide 11: Principal 2: Input Bias Current
Ideal Opamps have a infinite input impedance
Ideal Opamps should therefore have NO current should flow at inputs
Differential Mode: Input voltages relative to each other. Voltage different at terminals
Common Mode: Input voltages relative to ground. Same voltage at inputs

## Slide 12: Experiment 5: Input Bias Current
FINDING 2:
Opamps consume negligible amount of current at input – this makes math EASY!!

## Slide 13
Experiment 6: Output Current
Use 2 current sensing resistors to measure input and output current.
FINDING 4: Opamps can have huge current gain!

## Slide 14
Experiment 7: Output Impedance
Change load resistor until you get ½ of maximum output (Rail voltage ~ 14V)

## Slide 15: Principal 2: Negative Feedback
Can use negative feedback to control the gain.
With feedback, the opamp alters output so that input offset is between (+) and (-) input are the same
If (+) > (-), output raises to positive rail. Once output is within “Input Offset Voltage” of (+), then output = (+)
Gain = 1

## Slide 16: Experiment 8: DC Voltage Follower or Buffer
Don’t have to swing to rail. Only swing to 3.3V
Stay away from the rails for more accuracy

## Slide 17: Experiment 9: AC Voltage Follower or Buffer
HOMEWORK:
Create a voltage follower with a low frequency AC
Increase frequency and what happens to output when frequency is above 20 KHz?
Difference larger for 5V than 3.3V. Slew Rate?
Don’t have to swing to rail. Only swing to 5V

## Slide 18: Principal 3: Gain and Negative Feedback
Feedback can be used to create gain for an inverting configuration or a non inverting configuration
With feedback, the opamp alters output so that input offset is between (+) and (-) input are the same
Use a voltage divider to feedback a fraction of the output voltage
Cavet emptor: Opamp may have low noise. Resistors add noise (thermal). Choose them wisely

## Slide 19: Experiment 10: Inverting Amplifier
Inverting Gain = -R2/R1 = -100K/1K = 100
For 10mV input, output should be -10mVx100 = -1V
HOMEWORK:
Change input voltage. At what point does the voltage clip (i.e., hit the negative rail)
Change R2 and R3. What is the max gain you can get.
Introduce a small AC signal and see if gain is the same as DC gain
Huh?

## Slide 20: LTSPICE MINUTE: TRACE CALCULATION

## Slide 21: Experiment 11: Non-Inverting Amplifier
Non-Inverting Gain = 1+ R2/R1 = 1+ 10K/100 = 101
For 10mV input, output should be 10mx101 = +1.01V
HOMEWORK:
Same as inverting amplifier

## Slide 22: Finding 4: Current Sink
Will f**** you up!
Resistor needs to be low enough to sink current for Non-Inverting Opamp
~600 uV Peak-to-Peak
~600 uV Peak-to-Peak
Small Signal

## Slide 23: Single Supply
Opamps swing between Positive Rail and Negative Rail
For +Rail and –Rail, swing is around 0
Negative rails allows voltages to swing below 0
For single supply swing needs to be between +Rail and Gnd
Need to add ½ supply offset to input

## Slide 24: Experiment 12: Single Supply
What happens if –Rail is 0 (ground)? What happens to the swing?
AC Short
DC Block
Voltage Divider
AC Short
Gain = 1 + 10K/100 = 101
p = 10m x 101=1.01
pp = 2 x p = 2.02

## Slide 25: Experiment 13: Distortion
What happens If gain is too high?
Gain is 100x. Input is 80mV, Output is 8V.
Voltage swing is from 7.5V->0 and 7.5V -> 14
Not enough room to accommodate necessary swing so it clips at Rails

## Slide 26: OPAMP LIMITATIONS
Frequency Limitation – Gain Bandwidth Product
Frequency & Output Voltage Limitation - Slew Rate
Noise

## Slide 27: Experiment 14: Gain Bandwidth Product
Opamps gain vary with Frequency
20dB @ 100KHz
60dB @ 1KHz
1KHz & 100KHz
1KHz
dB = 20Log(992/10) = 40dB
100KHz
dB = 20Log(97/10) = 19.7dB
Gain = 20Log(100/10) = 40dB

## Slide 28: Experiment 15: Slew Rate
Will f**** you up!
10 KHz
20 KHz

## Slide 29: Experiment 16: SR Simplification
Homework: Add feedback to this circuit and measure time
Sharp Impulse at 100 us for 3m.

## Slide 30: Finding 4: Slew Rate Calculation
Slew Rate = 0.3 V/us = 300,000 V/s
For 13 Volts,
  F = SR/(2*PI*V) = 300,000 / (2 * 3.14 * 13) = 3.675 KHz
For 1 Volt, F = 47.771 KHz
For 5 Volts, F = 9.554 KHz
Homework: Create test circuit with gain and see how the output is impacted after these frequencies and voltages. **Don’t forget gain bandwidth product

## Slide 31: Principal 4: Opamp Noise
All amplifiers introduce noise into a circuit that reduces SNR.
4
1
Amplification x10
40
10
10 + amp_noise
Opamps introduce “White” Noise and “Pink” Noise. Noise is subject to gain with voltage and current noise added to input.
Feedback network introduces White Noise from resistors – Usually Largest
Opamp
Feedback Network
SNR = 4/1 = 4
SNR= 40/10+ < 4
Low F - PINK
Higher F - White
Spectral Noise Density

## Slide 32: Modeling Noise in Opamps
Current Noise and Voltage Noise
Resistor Voltage Noise
Resistor Voltage Noise
Resistor noise is about 4nV/rHz for 1K Resistor at room temp

## Slide 33: Experiment 17: Calculate Opamp Noise
At the output: Spectral Noise Density:
Noise from resistors:
  R1: 40nV/rHz
  R2: 400nV/rHz
LT1013 Opamp current noise
  7nV/rHz
LT1013 Opamp voltage noise
  2200nV/rHz
Sum of Squares: 2236 nV/rHz (2.2uV/rHz)
Bandwidth

## Slide 34: Experiment 18: Noise in Audio Range
Point to Trace Name and Press CTL-Click
Dumb it down: Multiply RMS noise by 6.6 to get peak-peak voltage
Peak-Peak Noise: 6.6x154uV = 1.02 mVpp

## Slide 35: NOISE WRAP UP
All amplifiers introduce noise into a circuit that reduces SNR.
4
1
Amplification x10
40
10
10 + amp_noise
Opamp
Feedback Network
SNR = 4/1 = 4
SNR= 40/10+ < 4
We now know how much noise opamp will add!!

## Slide 36: FIN