## Slide 1: Sideband Inversion, Carrier Suppression and all that...
Note: This is only applicable if you are designing your own Superhet Radio.
Kits and commercial radios account for sideband inversion

## Slide 2: How it Started?
Dueling 612’s Transceiver
Modified for Multiband and 12 MHz IF

## Slide 3: SIDEBAND INVERSION
Sometimes referred to as spectrum inversion
Swapping of LSB (Lower Side band) and USB (Upper Side Band) depending on how mixing is done
High Side Injection: Happens when LO (Local Oscillator) frequency is higher than incoming RF (Radio Frequency) input signal. Alternatively, IF (Intermediated Frequency) is lower that LO
  i.e., LO > RF, or IF < LO
You could start out with an UPPER sideband signal coming out of your sideband generator, then, after you mix it with your VFO (or Si5351!) you end up with a LOWER sideband signal.
Bill Meara, N2CQR
Sideband reversal occurs in mixing only if the signal with the modulation is subtracted from the signal that isn't modulated.
Joel Hallas, W1ZR

## Slide 4: Wikipedia Says….

## Slide 5: BACK TO BASICS: SUPERHETERODYNE RECEIVER
Mix incoming radio frequency (RF) signal (from Antenna) to an intermediate frequency (IF)
Use filter to limit bandwidth and improve selectivity
E.g., bandwidth of 700 Hz for CW, 3KHz for SSB
RF
IF
LO
Mixer
Bandwidth
Filter
Audio
BFO
Mixer
Used for Selectivity

## Slide 6: BACK TO BASICS: SUPERHETERODYNE TRANSMITTER
Mix/Modulate incoming audio signal (microphone) with a carrier (Oscillator) to an intermediate frequency (IF) which is RF
Filter IF to only pass desired sideband (i.e., supress carrier and other sideband)
Limit bandwidth to be transmitted
Mix IF with another Oscillator to generate desired RF to antenna
RF
IF (RF)
LO
Mixer
Bandwidth
Filter
Audio
Carrier
Mixer
Used to supress carrier and unwanted sideband

## Slide 7: BACK TO BASICS: MIXING
Fout = m x Fosc +/- n x Fin (for all m & n)
That is,
  Fout = m x Fosc – n x Fin
  Fout = m x Fosc + n x Fin
m and n represents harmonic number (1st harmonic, 2nd harmonic, etc.)
Let's only consider the fundamental frequency
Let's assume m=1 and n=1
  Fout1 = Fosc – Fin
  Fout2 = Fosc + Fin
Fin
Fout
Fosc

## Slide 8: CONVENTION
From here on I will be discussing frequency domain. It’s the output in a spectrum analyzer
In the time domain, we use an Oscilloscope which does not distinguish multiple frequencies
Frequency
This is showing 3 distinct frequencies present in the signal
SA display each frequency as a line (i.e., pure sine wave)
F1
F2
F3

## Slide 9: BACK TO BASICS: GENERATING SIDE BANDS
Let's mix (modulate) a carrier radio frequency (e.g., 7.1 MHz) with an audio frequency (e.g., 1500 Hz). Remember m=n=1 i.e., Fundamental only
  Fmd = Frf + Fa = Fc + Fa (USB)
  Fmd = Frf – Fa = Fc – Fa (LSB)
E.g.
  Fc + Fa (USB) = 7100000 + 1500 = 7101500 Hz
  Fc – Fa (LSB) = 7100000 - 1500 = 7098500 Hz
Fa
Fmd
Frf or Fc
Fa = Audio Frequency (e.g., 1500 Hz)
Frf or Fc = Radio Frequency Carrier (e.g., 7.1 MHz)
Fmd= Modulated Radio Frequency output
Fc
Fc + Fa
LSB
USB
Fc - Fa
Frequency
THIS IS VERY IMPORTANT!!
Note: USB and LSB are identical and can be interchanged

## Slide 10: SIDEBAND WITH AUDIO
Fc
Fc + Fa
LSB
USB
Fc - Fa
Frequency
Fc
Fc + Fa
Fc - Fa
RF Frequency
LSB
USB
Low Frequency Audio
(Closer to Carrier)
LSB is a reflection of USB and this is important when selecting BFO
High Frequency Audio
(Farther from Carrier)
High Frequency Audio
(Farther from Carrier)
Fa
Low Frequency Audio (say 100Hz)
High Frequency Audio (say 3KHz)
THIS IS VERY IMPORTANT!!
!!
Fa
Audio Frequencies
i.e., USB and LSB are identical but a mirror image

## Slide 11: SINGLE SIDEBAND SUPRESSED CARRIER TRANSMISSION
Fc + Fa
RF Frequency
USB
Low Frequency Audio
High Frequency Audio
Fc + Fa
RF Frequency
USB
LO
Placing LO on wrong side (and subtracting) will invert the audio.
LO
Low Frequency Audio
(Closer to Carrier)
High Side Injection
Low Side Injection
Carrier Suppressed

## Slide 12: LET'S BREAK IT DOWN

## Slide 13: FIRST MIXER: GENERATE IF
Recall for m=n=1, a mixer generates two frequencies:
  Fif = Flo + Frf
  Fif = Flo - Frf
Sideband inversion is only when LO is higher than RF or IF (i.e., LO > RF, or LO > IF)
If LO > RF, Need to subtract RF from LO to get IF
  Fif = Flo - Frf
  Fif = Flo + Frf (unwanted image)
If LO < RF, No inversion even if you subtract
Frf
Fif
Flo
Frf = Radio Frequency input (modulated carrier suppressed)
Flo = Local Oscillator Frequency
Fif = Intermediate Frequency
Flo
Frequency
Fif
Frf
Fif
(Image)
IF somewhere below LO

## Slide 14: FIRST MIXER: GENERATE MODULATED IF
Recall, for modulated carrier
  Fmd = Fc + Fa (USB)
  Fmd = Fc - Fa (LSB)
If we inject Fmd into mixer, what is the IF.
  Fif = Flo + Fmd
  Fif = Flo - Fmd
  Only focus on subtraction part of mixed artifact
  Fif = Flo – (Fc + Fa) (USB)
  Fif = Flo – (Fc - Fa) (LSB)
Expand and you get
  Fif = Flo – Fc - Fa (was USB)
  Fif = Flo – Fc + Fa (was LSB)
Buf Fif = Flo – Fc and so
  F1 = Fif - Fa (now LSB, was USB)
  F2 = Fif + Fa (now USB, was LSB)
Fmd
Fif
Flo
Fmd = Modulated Radio Frequency input (carrier supressed LSB/USB)
Flo = Local Oscillator Frequency
Fif = Intermediate Frequency
Fa = Audio Frequency that modulates carrier
Flo
Frequency
Fif
Fif + Fa
Fif - Fa
Was LSB now USB after mixing
Was USB now LSB after mixing
See
Slide 9
RF from
Antenna

## Slide 15: ALTERNATE VIEW
Fmd
Fif
Flo
Fmd = Modulated Radio Frequency input (modulated)
Flo = Local Oscillator Frequency
Fif = Intermediate Frequency
Flo
Flo
USB
Low Frequency Audio
High Frequency Audio
USB
Low Frequency Audio
High Frequency Audio
Fc
Frequency
High Frequency Audio
Low Frequency Audio
Fif
LSB
10
20
100
90
80
MINUS
EQUALS

## Slide 16: ADDRESS IN TRANSMIT CHAIN

## Slide 17: CARRIER SUPRESSION: Why is Sideband Inversion Important?
Fc
Fc + Fa
LSB
USB
Fc - Fa
Frequency
Fc
Fc + Fa
Fc - Fa
Frequency
LSB
USB
Low Frequency Audio
Low Frequency Audio
Need to remove the carrier and only select USB or LSB when receiving or transmitting
Answer: All radios transmit USB and LSB and not the inverted sideband….How do you to this?

## Slide 18: THE BANDWIDTH FILTER (Crystal Filter) Transmitter
Audio
IF1
Carrier
Mixer
Bandwidth
Filter
Radio Frequency
LO
Mixer
Fc
Fc + Fa
Fc - Fa
LSB
USB
Fc + Fa
USB
IF1
IF2
IF2
Filter Passband

## Slide 19: THE BANDWIDTH FILTER (Crystal Filter) Transmitter
Fc
Fc + Fa
Fc - Fa
LSB
USB
Crystal Filter Centre Frequency
(Resonant Frequency of Filter)
E.g., 4914507 Hz
Fc
Fc + Fa
Fc - Fa
LSB
USB
Fc equal to Filter centre frequency
Fc shifted 1500 Hz BELOW Filter centre frequency

## Slide 20: THE BANDWIDTH FILTER (Crystal Filter) Transmitter
To get proper orientation, need to “invert” Carrier.
  Filter USB to transmit LSB.
  Filter LSB to transmit USB
Audio
IF1
Carrier
Mixer
Bandwidth
Filter
Radio Frequency
LO
Mixer
IF2
If LO is higher than IF2, Sideband will be inverted.
i.e., RF=LO-IF2
Fc
Fc + Fa
Fc - Fa
LSB
USB
Fc shifted 1500 Hz ABOVE Filter centre frequency

## Slide 21: ADDRESS IN RECEIVE CHAIN

## Slide 22: The Bandwidth Filter (Crystal Filter) RECEIVER
Fc
Fc + Fa
USB
RF
IF
RF
IF
LO
Mixer
Bandwidth
Filter
Audio
BFO
Mixer
Filter Centre Frequency to only pass USB
Mixer shifts incoming RF to be within the filter passband
Need to shift Fc + centre of USB
USB
WHAT COULD HAPPEN HERE?
Sideband Inversion
Fshift
Fc

## Slide 23: The Bandwidth Filter (Crystal Filter) RECEIVER
Fc
Fc + Fa
USB
RF
IF
USB input to mixer
LSB output from the mixer
LSB
If LO above RF, the 1st Mixer inverts sideband
i.e., IF = LO - RF
Fc
Fshift
LO
Note: USB and LSB are identical and can be interchanged

## Slide 24: The Bandwidth Filter (Crystal Filter) RECEIVER
Fbfo
Fc + Fa
USB
RF
IF
LSB
Audio
BFO
Mixer
IF
Fbfo
Fbfo needs to be below or above signal in order to get low/high frequency orientation
Need to account for sideband inversion when determining BFO frequency
e.g., LSB, Fbfo = Filter Centre frequency + 1500 Hz
e.g., USB, Fbfo = Filter Centre frequency - 1500 Hz
Low Frequency Audio
High Frequency Audio
Low Frequency Audio
High Frequency Audio

## Slide 25
Ya gotta ask yourself one question
Do you know what causes sideband inversion and how to deal with it?
Well…Do ya punk?